## Slide 1: XRootD and Object Store: A new paradigm
Katy Ellis, Chris Brew, George Patargias, Tim Adye, Rob Appleyard, Alastair Dewhurst, Ian Johnson
4th November 2019
katy.ellis@stfc.ac.uk
Notes: HEP grid sites are interacting with XRootD in many different ways

## Slide 2: Introduction to XRootD and Ceph at RAL
Rutherford Appleton Laboratory (RAL) is the UK Tier 1
  Supports all LHC experiments and growing number of others in HEP, Astronomy and Space
RAL disk storage is known as Echo
  Based on Erasure Coded Ceph Object Store
  University of Glasgow is currently setting up a similar Ceph cluster
Access to Echo is primarily via XRootD
  The challenge is to optimize access for the different use cases
  Gridftp plugin, but intention is to phase out
Notes: Glasgow will also be using gridftp and xrootd plugins for Ceph access
Gridftp plugin and S3 for the future, but the storage is basically an ‘XRootD’ system on Ceph object store
Unique among Tier 1s, but likely to become more common

## Slide 3: Contents
Description of disk storage and XRootD at RAL
XRootD data access efficiency
  CMS-AAA (remote data access system)
  Job access
XRootD TPC
  Object-store particulars
  Delegation
XRootD authentication
  ALICE configuration

## Slide 4: XRootD interactions with Echo
data flow
External
x7
x800
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Ceph storage node
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Ceph storage node
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
x180
XRootD server
rados plugin
libradosstriper
GW container
XRootD client
User job
Job container
XRootD client
User job
Job container
XRootD cache
XRootD server
rados plugin
libradosstriper
GW container
XRootD client
User job
Job container
XRootD client
User job
Job container
XRootD cache
XRootD server
rados plugin
libradosstriper
GW container
XRootD client
User job
Job container
XRootD client
User job
Job container
XRootD cache
Worker Node
XRootD server
libXrdCeph
libradosstriper
Gateway container
XRootD client
User job
Job container
XRootD client
User job
Job container
XRootD cache
Gateway
XRootD server
libXrdCeph
libradosstriper
CMS-AAA-proxy
XRootD server
libXrdCeph
libradosstriper
x2

## Slide 5: Erasure coding
Divide each file into 64 MB ‘stripes’
  Then split into 8 x 8 MB objects called ‘shards’
  An additional 3 shards are calculated for redundancy
  The 11 shards are stored on 11 different servers
  Any 3 out of 11 shards can be missing or corrupted without data-loss

## Slide 6: Reconstruction of a stripe
Divide each file into 64 MB ‘stripes’
  Then split into 8 x 8 MB objects called ‘shards’
  An additional 3 shards are calculated for redundancy
  The 11 shards are stored on 11 different servers
  Any 3 out of 11 shards can be missing or corrupted without data-loss
1
2
3
4
5
6
7
8
9
10
11
2
3
4
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
11
1
3
4
5
7
8
9
11
Quickest shards
stripe
Gateway

## Slide 7: XRootD interactions with Echo
data flow
External
x7
x800
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Ceph storage node
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Ceph storage node
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
x180
XRootD server
rados plugin
libradosstriper
GW container
XRootD client
User job
Job container
XRootD client
User job
Job container
XRootD cache
XRootD server
rados plugin
libradosstriper
GW container
XRootD client
User job
Job container
XRootD client
User job
Job container
XRootD cache
XRootD server
rados plugin
libradosstriper
GW container
XRootD client
User job
Job container
XRootD client
User job
Job container
XRootD cache
Worker Node
XRootD server
libXrdCeph
libradosstriper
Gateway container
XRootD client
User job
Job container
XRootD client
User job
Job container
XRootD cache
Gateway
XRootD server
libXrdCeph
libradosstriper
CMS-AAA-proxy
XRootD server
libXrdCeph
libradosstriper
x2

## Slide 8: XRootD cache current setup
Disk caches on the Worker Nodes
Memory caches on the external Gateways
No cache on the CMS AAA
Notes: Data in memory cache is accessed very fast – stored in RAM – but only exists while the application is running (non-persistent)
Data in disk cache is less fast, but persists, as it is stored on the disk.

## Slide 9: CMS jobs and Echo
Goal – learn about and improve the I/O for jobs run at RAL
Notes: Containers in containers – with the proxy / gateway

## Slide 10: CMS jobs and Echo – test setup
Goal – learn about and improve the I/O for jobs run at RAL
RAL worker node, drained and isolated from the farm
  One job at a time
  Using the full containerized setup
  Submission via condor_submit
Various types of CMS jobs, previously run at RAL
  Chose to use an analysis job written by RAL colleagues for the main test
Adapted site configuration file
(CMS jobs have an added option of “cache-hint”)
Notes: Containers in containers – with the proxy / gateway

## Slide 11: CMS jobs and Echo
Echo
XRootD gateway
XRootD proxy
8 shards form stripes
‘File’ is cached and served to the job container
/pool/xcache/
Job
Worker Node Docker Containers
/pool/xcache/
XRootD client
User job
Job container
XRootD Gateway
XRootD Proxy
XRootD (manager)
Tested different values of ‘cache—hint’
These affect the way data is transferred to and stored in the job container
<application-only>, <lazy-download>, <storage-only>, <auto-detect>
File is mounted on the WN in case of repeat reads
Job received data through XRootD client
Stripes are concatenated to form the ‘file’, depending on requirement
.root
Worker node (WN)

## Slide 12: CMS jobs and cache-hint
Analysis job – making NTuple from 4 .root files with total size ~9 GB.
~10 tests for each cache-hint value.
Notes: Highest minus lowest gives some indication of the spread – not really enough statistics for standard deviation.
Not sure how to tell what ‘auto-detect’ is doing, other than inference from the numbers

## Slide 13: CMS jobs and cache-hint
~10 tests for each cache-hint value.
Analysis job – making NTuple from 4 .root files with total size ~9 GB.
Fairly tight distributions.
‘User’ time very similar for all tests except slightly greater for Storage-only.
Auto-detect appears to choose Application-only.
Lazy-download (used currently at RAL) is slowest.
However…this is one job (type).
What about when multiple jobs running simultaneously?
Reliability is a concern.
Cache-hint | Mean total (min:sec) | Highest - lowest | NetworkInputMb
Application-only | 32:11 | 1:45 | ~6900
Lazy-download | 36:04 | 1:25 | 9173
Storage-only | 35:15 | 1:46 | ~6680
Auto-detect | 32:13 | 1:47 | ~6900
Notes: Highest minus lowest gives some indication of the spread – not really enough statistics for standard deviation.
Not sure how to tell what ‘auto-detect’ is doing, other than inference from the numbers
Hoping to spend a lot more time on this

## Slide 14: XRootD Third Party Copy (TPC) and Echo
As Echo is an object store, the path name has to be specified exactly
For example, if this ‘path’ was used to write or read
  root://xrootd.echo.stfc.ac.uk:1094/dteam:test1/testKaty1
XRootD can replace the slash with a double slash
  root://xrootd.echo.stfc.ac.uk:1094//dteam:test1/testKaty1
To accept either path, and not rely on other sites to provide only pathnames with single slashes, a workaround was applied at RAL
  Define additional paths with extra slashes in the authdb and then translate them back in the TFC (Trivial File Catalogue)
Two different object names in Echo
tim.adye@stfc.ac.uk
Notes: TFC is normally only for CMS – but in this case it is being used by all experiments to get around this problem
Minor issues remain, Xrd, but related to RAL

## Slide 15: XRootD Third Party Copy (TPC) and Echo
Concerning authentication, this setup requires the use of delegation of the command issuer’s credentials to the destination server, e.g.
  xrdcp --tpc delegate only root://xrootd.echo.stfc.ac.uk:1094/dteam:test1/testSourceFile root://griddev03.slac.stanford.edu:2094//xrootd/atlas/tpctest/testDestFile [140B/140B][100%][==================================================][35B/s]
Notes: Other changes specific for Echo in this slide. Tim believes everyone is now using ‘delegate only’ – but at the time not so much
Additional diagram of the xrootd proxy

## Slide 16: CMS AAA and Echo
CMS AAA is a service to deliver ”Any data, any time, anywhere” to jobs running at any CMS site.
Partial reads are common in CMS but not efficient for object store – Echo works best when serving whole stripes (64 MB section of a file).
  Much more data into proxy than out!
Unclear whether (disk) caching is helpful – we believe the XRootD cache was demanding whole file, even if data from only a small number of stripes was requested.
As a result – overloaded service that required frequent intervention.

## Slide 17: CMS AAA and Echo
AAA proxy cache was turned off.
More recent CMS files now store the metadata in one place near the start or end of files, instead of dispersed throughout.
Service is now much more stable and rarely requires intervention
External
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Ceph storage node
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
CMS-AAA-proxy
XRootD server
libXrdCeph
libradosstriper

## Slide 18: ALICE and Echo
ALICE require their own XRootD authentication plugin
Blocker for ALICE to move from CASTOR onto Echo
The source code was modified to accommodate the pool name alice:/
ALICE transfers are currently somewhat isolated from other VOs
  Have their own Echo gateways
  Have their own XRootD alias: alice.echo.stfc.ac.uk
george.patargias@stfc.ac.uk

## Slide 19: Summary
Echo is working effectively with XRootD
  Looking for continuous improvement
All four LHC experiments are up and running
  Each saw their own individual issues
Non-LHC experiments are also, or will soon, use Echo for disk storage
Thanks to the XRootD developers for their collaboration!

## Slide 20: Backup
Notes: From Michel Simon’s talk: pfc.blocksize (large buffer for whole file streaming vs small for vector reads)
Pfc.ram – how much RAM to use for buffer
pfc.diskusage 0.89 0.90 purgecoldfiles 2d 5

## Slide 21: CMS jobs and Echo – XRootD proxy config
Located on the WN : /etc/xrootd/xrootd-ceph.cfg
Matches the Echo stripe size:
  xrootd.async segsize 67108864
  xrd.buffers maxbsz 67108864
pfc = proxy file cache
  pfc.ram 7g
  pfc.blocksize 16m
Notes: From Michel Simon’s talk: pfc.blocksize (large buffer for whole file streaming vs small for vector reads)
Pfc.ram – how much RAM to use for buffer
pfc.diskusage 0.89 0.90 purgecoldfiles 2d 5

## Slide 22: Cache-hint options
application-only
  This is the default and means ROOT will do the caching. If PoolSource.cacheSize is non-zero, a TTreeCache of that size will be created per open file. Asynchronous read-ahead will be turned off and the cache will be filled with normal reads.
storage-only
  Means ROOT will drive the caching using a prefetch list, but will not allocate a cache of its own. If PoolSource.cacheSize is non-zero, a TTreeCache with a read-list of that size will be created, but no actual cache buffer -- the ROOT cache will be "virtual" and could in fact be very large. ROOT will hand over the prefetch list to the storage layer, which is expected to do its own caching. This method only makes sense if the underlying storage binding is capable of prefetching, which is currently true for local files (and anything downloading into a local file, such as srm, storm, gsiftp) and RFIO. Using this method with an incompatible storage system such as dCache will trigger an error.

## Slide 23: Cache-hint options
lazy-download
  Means remote files will be downloaded to a local shadow file on demand in 128MB segments. ROOT reads will be directed to this local file; ROOT will never read directly from the remote file. If PoolSource specifies a non-zero cache, it will behave as a "storage-only" virtual / prefetch cache. Note that the file will be downloaded lazily even if PoolSource.cacheSize is zero. The local shadow file will be created in the specified temporary directory and will be removed automatically when the corresponding remote file is closed. If no suitable local temporary directory with sufficient free space can be found, lazy download is automatically switched off.
auto-detect
  This tells the I/O layer to pick the best strategy suited for the I/O technology in use. This will be "lazy-download" for RFIO, dCache and the "file" protocol, including any method which downloads remote files to local disk.

## Slide 24: Changes required for TPC // problem
authdb:
# VO = Atlas
u atlasprod \atlas:datadisk/ a \atlas:scratchdisk/ a /atlas:datadisk/ a /atlas:scratchdisk/ a
u atlasuser \atlas:datadisk/ r \atlas:scratchdisk/ a /atlas:datadisk/ r /atlas:scratchdisk/ a
New xrootd storage.xml
<lfn-to-pfn protocol="direct" path-match="/*(.*)" result="$1"/>

## Slide 25: CMS jobs and Echo
MC production
RAW
CMS detector
(Full) SIM
DIGI
Digitization
RECO
AOD
Analysis
Notes: https://indico.desy.de/indico/event/3246/session/2/material/1/3.pdf
What are the most important things to look at wrt echo data access